## Slide 1: Fluvial Geomorphology: A GIS toolbox to extract raster data along spatial continuum
Lepoutre A., Research Assistant, Department of Geography, McGill University, Montreal
Developed in collaboration with phD Fabien Hugue under the supervision of Prof. Michel Lapointe.

## Slide 2: NSERC HydroNet
“Hydropower is a leading source of electricity in Canada.
NSERC HydroNet is a national research network aimed at promoting sustainable hydropower and healthy aquatic ecosystems in Canada.
The general objectives of the network are to increase our understanding and develop new tools to better assess, minimize, and mitigate the effects of hydropower on fish and their habitats.”

## Slide 3: HydroNet study sites

## Slide 4: Example of in-situ habitat mapping

## Slide 5: Example of in-situ habitat mapping
Can we assess habitat quality, damming impact for many rivers only with field data??

## Slide 6: General objectives
Develop novel approach using remote sensing to describe meso, reach and 10km river scale habitat structure.
Understand the meso, reach and 10km river scale patterns of physical habitat variables (width, depth, slope, velocity, grain size, LOD, …)
Study specific reaches where fish habitat variables (wetted width, spawning sites, substrate embeddedness, riparian vegetation,…) are more likely to be impacted by damming
Assess river reach sensitivity to damming

## Slide 7: Solution: remote-sensing habitat assessment
Segmentation of the river stretch depending on the morphology
300 m
 4 identifiable sections

## Slide 8
300 m
Section 1
Section 2
Section 3
Section 4
Solution: remote-sensing habitat assessement
Morpho-Type 1 (section 1, 4): Wide, deep, slow, mostly composed of massive pools
Morpho-Type 2 (section 2): Complex Pool-Riffle system
Morpho-Type 3 (section 3) : Straight, narrow and steep
 Standardized method

## Slide 9: Specific (tools) objectives
Extract and organize data in analytical way for different rivers, at different scales
Use relevant geometries for calculation of various parameters (fixed vs dynamic).
Flexible vector/raster/tabular data interactions
Automated method
Somewhat robust, large data loads
User-friendly

## Slide 10: Inputs
Dam
Flow direction
(1) WorldView-II Satellite image:
Multispectral: 8 Bands (VIS-NIR) / 2 m res.
Panchromatic: 50 cm res.

## Slide 11: Inputs
(2) Watermask/spatial corridor
Dam
Flow direction

## Slide 12: Inputs
Dam
Flow direction
(3) River centerline/baseline

## Slide 13: Inputs
(4) Raster: Depth map
-> field data for calibration + raster calculation
Inputs
(3) Depth map (ENVI method)

## Slide 14: Create Transects
Cross-sections provide adequate geometry for fixed hydraulic and geomorphologic parameters (d & Q =>modelled v, channel width, # of channels,..).
Spatially discrete data: good for designing, mapping and validation of field surveys, in which surveyed path/areas can meander and change widths.
Provide an intra-river spatial reference system
=> transects create inputs for other tools.

## Slide 15: Transects along centerline solutions
Many applications => many solutions
  Hydraulic research RivWidth from Tamlin
  Coastal erosion/accresion research (DSAS,“Beach tools”,...)
  Gerry Galbrisch arc9.3 solution
  Custom solution => slope extraction in meandering environment optimized

## Slide 16: Create Transects
Fluvial Geomorphology’ transects specifics:
Many rivers => many situations. Implementation where slope calculation handles sinuosity well
For field work: option to create transects
Need transects to be clipped

## Slide 17: Create Transects – Slope extraction

## Slide 18: Create Transects – Slope extraction

## Slide 19: Transects: Resulting outputs (1)
River width profile:

## Slide 20: Transects: Results (2)
2D Velocity estimates:
Continuity equations
Based on data extracted by cross-sections on the image
(Manning’s law, Du Boys, Log profile law)
Interpolation with barriers
Velocity raster
Depth map + Discharge + Transects

## Slide 21: Transects: Results (3)
Habitat 1: Deep and slow (Pools)
Habitat 2: Medium depth and
fairly rapid (Runs)

## Slide 22: Transects: Results (3)
Illustration for Depth-Velocity optima of a generic fish (Brook Trout)
Global river morpho. : yield parameters for Moving Window

## Slide 23: Moving Window Solutions
Hawth’s tool: roving window…arc9.3 and discontinued
Thomas Dilts' Stream Gradient and Sinuosity Toolbox…never worked for me "Invalid Tool: Unable to execute the selected tool" ..designed in 9.2

## Slide 24: Moving Window
Provide: 1) fixed “entities” of data on which statitics and metrics can be calculated 2) entities have location that allows them to be related spatially to a reach, river scales.
Overlap of polygons provide smoothing of stream of data, possibility of dynamic visualization => global trends & local trends.
Continuous data => More complex metrics for habitat characterization not necessarily visually obvious (modal peak, Hydro-Morphological Index of Diversity, % of pixels outside boxes defined from global bivariate,..) .

## Slide 25: Moving Window - Inputs/Outputs & Implementation
Inputs:
-specific parameters
-water polygon
-transects
-Centerline
-Rasters
Outputs:
-raster pixel values in text
file for each polygon
-polygon shp
Exported .txt files

## Slide 26: Moving Window .Shp Output

## Slide 27: Moving Window - Results
Dam
Flow direction
Section 3: Deep and slow (Pools)
Section 2:
Medium depth and fairly rapid (Runs)
Section 1:
Medium to high d and slow v

## Slide 28: Moving Window - Results (1) Bivariate histogram

## Slide 29: Moving Window – Results (1)
300 m
1
2
3
4
Mississagi river, ON

## Slide 30: Moving Window - Results (1)
Section 2: Variable, shallow
300 m
1
2
3
4

## Slide 31: Moving Window - Results (1)
300 m
Section 3: Straight, narrow
1
2
3
4
300 m
1
2
3
4

## Slide 32: Moving Window - Results (1)
300 m
Section 4: Large deep pools, slow
1
2
3
4

## Slide 33: Moving Window – Results (2) Metrics
Metrics
Modal velocity
Modal depth
River width
Width/Depth ratio
Homogeneity factor
Heterogeneity (Entropy)
Heterogeneity (HMID)
Fast-Shallow Habitat
Slow-Shallow Habitat
Slow-Deep Habitat

## Slide 34: Moving Window – Results (2) Metrics
Section 3: Deep and slow (Pools)
Section 2:
Riffles
Section 1:
small Pools
But 4th section: Complex transition zone not necessarily obvious to the eye

## Slide 35
Local Moving Window
Same principle but usability is more in field work validation:
Field data delimited by couples of points (or objects)
Creates polygons and exports underlying raster data to .txt file similarly to Moving Window
Reach covered by polygon can be increased => fish movement
=> In our case: used to validate biology and morphology database from field

## Slide 36
Local Moving Window

## Slide 37
Local Moving Window –Shp Output

## Slide 38: Distance Along Line (DAL)
=> Cumulative distance system along centerline.

## Slide 39: Method summary
Stats!!

## Slide 40: Conclusion
Fluvial Geomorphology toolbox provides:
Fixed & dynamic geometries for different metric calculation
Field work validation
Simple geometries increase usability, good for academia
Perspectives:
-Inter-region habitat variability study & Regulated Vs. Natural rivers
More images -> can Python and arcpy module handle it?
=>open source solution using GDAL & OGR, .Net (C#)?

## Slide 41: Toolbox availability
Toolbox availability
adrienlepoutre.com/Downloads/
McGill U. GIC website
adrienlepoutre@mail.mcgill.ca